## Slide 1
Capacity Planning
For Products and Services

## Slide 2: Capacity Planning
Capacity is the upper limit or ceiling on the load that an operating unit can handle.
Capacity also includes
  Equipment
  Space
  Employee skills
The basic questions in capacity handling are:
  What kind of capacity is needed?
  How much is needed?
  When is it needed?

## Slide 3: Importance of Capacity Decisions
Impacts ability to meet future demands
Affects operating costs
Major determinant of initial costs
Involves long-term commitment
Affects competitiveness
Affects ease of management
Globalization adds complexity
Impacts long range planning

## Slide 4: Capacity
Design capacity
  maximum output rate or service capacity an operation, process, or facility is designed for
Effective capacity
  Design capacity minus allowances such as personal time, maintenance, and scrap
Actual output
  rate of output actually achieved--cannot exceed effective capacity.

## Slide 5: Efficiency and Utilization
Actual output
Efficiency =
Effective capacity
Actual output
Utilization =
Design capacity
Both measures expressed as percentages

## Slide 6: Efficiency/Utilization Example
Actual output = 36 units/day
Efficiency = = 90%
Effective capacity 40 units/ day
Utilization = Actual output = 36 units/day
= 72% Design capacity 50 units/day
Design capacity = 50 trucks/day
Effective capacity = 40 trucks/day
Actual output = 36 units/day

## Slide 7: Determinants of Effective Capacity
Facilities
Product and service factors
Process factors
Human factors
Policy factors
Operational factors
Supply chain factors
External factors

## Slide 8: Calculating Processing Requirements
If annual capacity is 2000 hours, then we need three machines to handle the required volume: 5,800 hours/2,000 hours = 2.90 machines

## Slide 9: Evaluating Alternatives
Cost-volume analysis
  Break-even point
Financial analysis
  Cash flow
  Present value
Decision theory

## Slide 10: Cost-Volume Relationships
Amount ($)
0
Q (volume in units)
Total cost = VC + FC
Total variable cost (VC)
Fixed cost (FC)

## Slide 11: Cost-Volume Relationships
Amount ($)
Q (volume in units)
0
Total revenue

## Slide 12: Cost-Volume Relationships
Amount ($)
Q (volume in units)
0
l
BEP units
Profit
Total revenue
Total cost
Loss

## Slide 13: Cost- Volume Analysis
Total Cost, TC= Fixed cost+ variable cost
Variable Cost= No of units produced (Q)* Variable cost per unit
Total Revenue, TR= No of units produced (Q)* Price per unit
Profit= Revenue-Cost= (TR-TC)
Break Even, TR=TC

## Slide 14
The owner of Old-Fashioned Berry Pies, S. Simon, is contemplating adding a new line of pies, which will require leasing new equipment for a monthly payment of $6,000. Variable costs would be $2 per pie, and pies would retail for $7 each.
a. How many pies must be sold in order to break even? b. What would the profit (loss) be if 1,000 pies are made and sold in a month? c. How many pies must be sold to realize a profit of $4,000? d. If 2,000 can be sold, and a profit target is $5,000, what price should be charged per pie?
FC=$6000
v=$2 per pie
R=$7 per pie
QBEP= FC/R-v =6000/(7-2)= 1200 pies/month
P=RQ – (FC+Qv) = 1000*7 – (6000+ 1000*2) = $ (-1000)= loss
Q = (P+FC)/(R-v) = (4000+6000)/(7-2) = 2000 pies
R=(P+(FC+Qv))/Q= (5000+(6000+2000*2))/2000= $7.5 per pie
TR=R*Q
or 23000=0.9*Q
Q=23000/0.9
Page 212, prob. 3

## Slide 15
A manager has the option of purchasing one, two, or three machines. Fixed costs and potential volumes are as follows: Number of Machines Total Annual Fixed Costs Corresponding Range of Output 1 $ 9,600 0 to 300 2 15,000 301 to 600 3 20,000 601 to 900 Variable cost is $10 per unit, and revenue is $40 per unit. a. Determine the break-even point for each range. b. If projected annual demand is between 580 and 660 units, how many machines should the manager purchase?
QBEP (1)= FC/R-v= 9600/(40-10)=320 units
QBEP (2) = FC/R-v=15000/(40-10) = 500 units
QBEP (3) = FC/R-v=20000/(40-10) = 666.7 units
It is observed that the break-even point is 500, which is in the range 301 to 600. This means that even if demand is at the low end of the range, it would be above the break-even point and thus yield a profit. That is not true of range 601 to 900. At the top end of projected demand, the volume would still be less than the break-even point for that range, so there would be no profit. Hence, the manager should choose two machines.

## Slide 16
A manager must decide how many machines of a certain type to purchase. Each machine can process 100 customers per day. One machine will result in a fixed cost of $2,000 per day, while two machines will result in a fixed cost of $3,800 per day. Variable costs will be $20 per customer, and revenue will be $45 per customer. a. Determine the break-even point for each range. b. If estimated demand is 90 to 120 customers per day, how many machines should be purchased?
Machine
1
2
Fixed cost
$2000
$3800
Process
0 to 100
101 t0 200
QBEP (1)= FC/R-v= 2000/(45-20)= 80 customers
QBEP (2) = FC/R-v=3800/(45-20) = 152 customers